## Slide 1: Raspberry Pi Master Class Day-19
Touch screen display Interface with RPi

## Slide 2: 01 Table of Contents 03 04 02
Interfacing Touch screen
Practical session
Touch Screen Display
Overview
Discussion, Tech news
Interractive session
Installing Packages
Practical

## Slide 3: PREREQUISITES FOR THIS SESSION
Raspberry Pi 3 Model b/B+
16 GB SanDisk class 10 SD Card
Card reader
Laptop with Internet
Power Adapter – 5V 2Amps
USB B-Type Cable
3.5” LCD Touch screen

## Slide 4: Touch screen LCD Display…
This small 3.5 inch touch screen Raspberry Pi Display module is designed especially for Raspberry Pi, using the latest Linux Core system.
The module sits right on top of Pi and an ideal alternative solution for HDMI monitors.
The screen also comes with a stylus to interact with the small screen.
LCD Type: TFT.
Touch Screen Type: Resistive Screen.
Backlight: Yes, LED.
Resolution (Pixel): 320 x 480.
Aspect Ratio: 8:5.
Touch Controller: XPT2046.

## Slide 5: PinOut
1, 17 3.3V 3.3V power input
2,4 5V 5V power input
3,5,7,8,10,12,13,15,16 NC No connection – used for support
6,9,14,20,25 GND Ground
11 TP_IRQ Active low interrupt pin for touch screen
18 LCD_RS Register select pin of Display controller
19 LCD_SI SPI data input for the LCD display
21 TP_SO SPI data output from the LCD display
22 RST Reset
23 LCD_SCK Clock sync pin of SPI communication
24 LCD_CS Chip select pin of SPI LCD
26 TP_CS Chip select pin of SPI Touch screen

## Slide 6: DEMO SESSION

## Slide 7: Configuration
sudo raspi-config
System options -> Boot Options -> Desktop/CLI -> Desktop Autologin Desktop GUI
Ok
Interfacing options -> SPI
Enable SPI – Yes
sudo rm -rf LCD-show
git clone https://github.com/goodtft/LCD-show.git
chmod -R 755 LCD-show
cd LCD-show/
sudo ./LCD35-show
Sudo reboott
cd LCD-show/
sudo dpkg -i -B xinput-calibrator_0.7.5-1_armhf.deb
Preference -> Calibrate Touchscreen.

## Slide 8
Q19 – Discussion
Dynamics
Kinematics – Motion of object without reference to forces
Dynamics – Forces and their influence on the motion of objects
Force, mass, momentum, energy

## Slide 9
Q19 – Discussion
Quantum Theory ?
Rocket Science

## Slide 10: Supercomputer HPE-Cray EX to Rank Among World’s Fastest; Will Help Study Climate Change, Wildfires, More
The HPE-Cray EX supercomputer will theoretically be able to perform almost 20 quadrillion calculations per second — 3.5 times faster than the existing machine at the NCAR-Wyoming Supercomputing Center.
Tech News - 19
Jan - 2021

## Slide 11: Thanks!
learn.pantechsolutions.net
“A Person who never made a mistake never tried anything new”
-Albert Einstein
www.pantechsolutions.net